## Slide 1: ASPEN Staged Separation Unit-Ops Samaa Zaman, Lane Crofton, Elina Tabarzadi, Tran Do and Michael Schachter CHBE446: Design 2 5 February 2024

## Slide 2: Introduction: Stage Separation Unit-Ops
Industrial Uses:
  Purify desired components
  Removing impurities and pollutants
Major unit-ops include:
  Distillation Columns
  Absorption Columns
  Stripping Columns
Notes: s

## Slide 3: Relevance to Ammonia Synthesis
Undesirable pollutants produced
  Primarily CO2
  Removed via separation techniques prior to reactor to prevent catalyst poisoning
The removal of carbon dioxide is commonly performed using a combination of absorption and stripping columns

## Slide 4: Carbon Dioxide Removal Techniques
Carbon dioxide can be removed via both physical and chemical absorption/stripping
Industrially, chemical methods have been preferred
  Leads to minimize waste of hydrogen
Common solvents used in the chemical absorption/stripping process include:
  Monoethanolamine (MEA)
  Potassium Carbonate (K2CO3)

## Slide 5: ASPEN Physical Absorption Column: Basic Setup
Step 1: Begin new ASPEN simulation
Step 2: Add all components from process
Step 3: Choose a property base method that best fits your components
  Ex. Wilson which utilizes Henry’s Law

## Slide 6: ASPEN Physical Absorption Column: Simulation Setup
Step 1: Add RADFRAC column to flowsheet
Step 2: Add 2 inlet streams to RADFRAC column
  Can be useful to label as liquid and gas feed
Step 3: Add both a distillate and bottoms stream
  For absorption the “distillate” is the desired vapor product with impurities removed

## Slide 7: ASPEN Physical Absorption Column: RADFRAC Setup (1)
Step 1: Define properties of both inlet streams based upon process information
  Includes flow rates, composition, temperature, pressure, etc.
Step 2: Under the configuration tab for the column, choose the following options

## Slide 8: ASPEN Physical Absorption Column: RADFRAC Setup (2)
Step 1: Under the streams tab for the column, choose the following options
  Liquid feed should enter at the top of the column
  Gas feed should enter at the bottom

## Slide 9: ASPEN Physical Absorption Column: RADFRAC Setup (3)
Step 1: Under the pressure tab for the column, enter the operating pressures for both stages
  This will depend on the process being used
  Ex. operating close to atmospheric pressure

## Slide 10: ASPEN Physical Absorption Column: RADFRAC Setup (4)
Step 1: On the side panel navigate to Blocks -> Your RADFRAC Column -> Column Internals
Step 2: Select Add New and double click on the new internals
Step 3: Scroll to the right and select the view option

## Slide 11: ASPEN Physical Absorption Column: RADFRAC Setup (5)
Step 1: Fill out the following screen based upon the specifications of your desired packing materials
Make sure that the rating option is selected, otherwise you will have incomplete errors

## Slide 12: ASPEN Physical Absorption Column: RADFRAC Setup (6)
Step 1: On the side panel navigate to Blocks -> Your RADFRAC Column -> Rate-Based Modeling
Step 2: Check the box for Rate-based calculation
Step 3: Run your simulation!

## Slide 13: ASPEN Chemical Absorption Column: RADFRAC Setup (1)
Choose the Electrolytes Template

## Slide 14: ASPEN Chemical Absorption Column: RADFRAC Setup (2)
Step 1: Under Properties, components; Input the required components for the process.
Step 2: Choose the Elec Wizard option to define the ionic species and salts that can be generated from the base components.

## Slide 15: ASPEN Chemical Absorption Column: RADFRAC Setup (2)
Step 1: Under Methods, choose ELECNRTL, which is electrolyte NRTL model with Redlich-Kwong EOS.

## Slide 16: ASPEN Chemical Absorption Column: RADFRAC Setup (3)
Step 1: Select the base components for electrolyte chemistry generation.
Step 2: Select Hydrogen ion type.
Step 3: Include salt formation and water dissociation reaction.

## Slide 17: ASPEN Chemical Absorption Column: RADFRAC Setup (4)
Step 1: Remove not relevant generated
Species and their reactions

## Slide 18: ASPEN Chemical Absorption Column: RADFRAC Setup (5)

## Slide 19: ASPEN Chemical Absorption Column: RADFRAC Setup (6)
Step 1: Under Chemistry, Global; Verify the reactions from Elec Wizard.
Step 2: Add any additional reaction with New button.
Step 3: Choose reaction type, and insert component and coefficient.

## Slide 20: ASPEN Chemical Absorption Column: RADFRAC Setup (7)
Step 1: Build the process flow diagram using the Radfrac ABS unit model.
Step 2: Specify the process inlet streams.

## Slide 22: ASPEN Chemical Absorption Column: RADFRAC Setup (8)
Step 1:On the set up page of Radfrac, select Rate-Based.
Step 2: Input the number of stages.
Note: Equilibrium model does not enable determining the options for parameters such as type and amount of packed bed.
Step 3: Select the best convergence based on the 2-phase mixture.

## Slide 23: ASPEN Chemical Absorption Column: RADFRAC Setup (9)
Step 1: Under the stream tab, input the feed(s) stage entry location and convention.
Note: The top stage in Aspen Plus is always 1. So the Liquid feed enters above-stage 1. On-stage, enters the other feeds to that specified stage.
Step 2: Input the product stream output stage.

## Slide 24: ASPEN Chemical Absorption Column: RADFRAC Setup (10)
Step 1: Under the pressure tab, enter the operating pressure for stage 1.
Pressure drop and other stages pressure, is optional.

## Slide 25: ASPEN Chemical Absorption Column: RADFRAC Setup (11)
Step 1: Under Column internals, define a new (INT-1).
Step 2: Enter the start and end stage of the section, packed height and diameter.
Step 3: Change Mode from default to Rating.
Step 4: Choose the best internal and Packing type for the mixture.

## Slide 26: ASPEN Chemical Absorption Column: RADFRAC Setup (12)
Step 1: Under the Rate- based modeling, select rate-based set up.
Step 2: For flow model select mixed, or counter current.
Note: In the mixed flow model, bulk properties for each phase are the same as outlet condition. In the counter-current, the properties of each phase are an average of the inlet and outlet.